## Slide 1
NUMA - Hardware and Software Technology
Notes: 1
1
This is one option for your presentation title page. Use when only title of presentation is needed.
Title and Bullets are in Reflex Blue which are defined as the following HSL numbers in Power Point:
H: 41121
S: 65520
L: 30704

## Slide 2
NUMA - Hardware and Software Technology
Geoff Hall
Senior Engineer, SCO Platform Products Division
Notes: 2
2
This is another option for your presentation title page when name and title of presenter are desired..

## Slide 3
Presentation Overview
NUMA hardware
Impact on O/S and applications
Implications for developers
Notes: 3

## Slide 4
NUMA hardware
What it is
Why it’s useful
Alternatives
A Close Up Look at the Intel space
Example Hardware
Notes: 4

## Slide 5
Review - what SMP is
Cache
Cache
uProc
uProc
Main Memory
I/O
Symmetric Multi Processor
Notes: 5

## Slide 6
SMP characteristics
Shared Everything
  Each processor has identical view of memory, I/O, disks, maybe interrupts
Mature technology
Limited scalability
  Memory bandwidth
  Need to keep all caches in-sync
  Scalability typically comes at greater entry cost
Notes: 6

## Slide 7
Review - what MPP is
Massively Parallel Processing
Proc
Notes: 7

## Slide 8
MPP characteristics
“Shared Nothing” (usually)
  High bandwidth message passing.
Immature technology
  No clear winner
  Limited software base
Uneconomic at low end
  Scalability is of limited use if entry cost is high
Notes: 8

## Slide 9
What NUMA is
Main Memory
Cache
Proc 1
Interconnect
Cache
Cache
Cache
Main Memory
Proc 2
Proc 3
Proc 4
Board A
Board B
Notes: 9

## Slide 10
NUMA Memory Map
Each processor sees the same memory map...
but the access times will differ
0
n
2n
Memory
addresses
Memory from board A
Memory from board B
Notes: 10

## Slide 11
NUMA and Cache Coherence
A NUMA system may or may not be Cache Coherent but...
ccNUMA (Cache Coherent NUMA) is most popular variant
  Reduced requirements on software (should be able to run SMP O/S unchanged).
  Cost is additional hardware complexity.
  Gemini targets ccNUMA platforms only.
Notes: 11

## Slide 12
NUMA Interconnects
Typically hierarchical, directory based
Popularity of SCI or derivatives
  SCI = Scaleable Coherent Interface, IEEE std
  Roughly, a server area network
  Various implementation technologies
  Various topologies
Notes: 12

## Slide 13
NUMA Characteristics
A “shared everything” model
  Programming model as per SMP
Maturing technology
  A subject of R&D for many years, but now the economics and technology look right
Promises greater scalability than SMP
  Depends on details of hardware, software
Notes: 13

## Slide 14
Motivations
SMP scaling difficulties
  It gets difficult and expensive to create large, scaleable SMPs
MPP programming difficulties
  Various MPP styles haven’t reached critical mass
Desire to exploit commodity hardware
  Hope is to use commodity parts with a small amount of additional glue
Notes: 14

## Slide 15
Where NUMA fits
Number of processors
1
10
100
1000
Conventional SMPs
NUMA Machines
MPP Machines
Notes: 15

## Slide 16
NUMA Advantages
It looks like a big SMP
  Leverage SMP application base
  Well understood programming model
  Easy administration
Excellent scalability story, especially for high-end
Very plausible winner in the marketplace
Notes: 16

## Slide 17
NUMA Disadvantages
It looks like a big SMP
  Fault tolerance issues
    Resilience typically through rapid reconfiguration and reboot
  If you don’t really need SMP there may be more appropriate alternatives
Economics of low end
  If you don’t need scalability, conventional SMP may be more appropriate
Not yet proven in mass market
Notes: 17

## Slide 18
Alternatives
High End SMPs,
Clusters
  Shared Disk
  Shared Nothing
    various degrees of coupling, interconnect speed
Low End MPPs
Variants (such as COMA, as pioneered by KSR)
Notes: 18

## Slide 19
NUMA for Intel systems
Some additional wrinkles
  Compatibility, I/O space, APICs etc.
Promising commercial prospect
  Exploitation of volume hardware, software
Need for some commonality
  Don’t want a major porting effort for each new piece of hardware
Notes: 19

## Slide 20
More Intel considerations
I/O tends to be PCI on a per-node basis
  Additional asymmetry to be dealt with
32 bit address space limitations
  But Pentium Pro has 36 bit physical address capability
Acknowledgment
  The following section has been based in part on material supplied by Data General
Notes: 20

## Slide 21
Example NUMA System
NUMA
Node
NUMA
Node
NUMA
Node
SCI Ring
SCI Ring
1GB/sec supporting up to 8 nodes
NUMA
Node
This slide courtesy of Data General
Notes: 21
21

## Slide 22
SHV Node Architecture
SHV Node
PPro cpu
L2 Cache
MC
PPro cpu
L2 Cache
PPro cpu
L2 Cache
PPro cpu
L2 Cache
PB
PB
PCI
Memory
B
B
B
DAC
SHV = “Standard High Volume”
  Quad Intel Pentium Pro processors and 82450 chipset
  Standard PCI based I/O
  P6 bus connector for cluster attachment (e.g. SCI NUMA)
This slide courtesy of Data General
Notes: 22
22

## Slide 23
SHV NUMA Node Architecture
Dual SCI Rings
Link Chip
Link Chip
Fabric Interface
SCI Directory
SCC
PIU-A
Snoop
RAM
Far Memory
Cache
PIU-D
SCI Interconnect Adapter
B-Link
SHV Node
PPro cpu
L2 Cache
MC
PPro cpu
L2 Cache
PPro cpu
L2 Cache
PPro cpu
L2 Cache
PB
PB
PCI
Memory
B
B
B
DAC
This slide courtesy of Data General
Notes: 23
23

## Slide 24
Far Memory Caches
Reduce the non-uniformity of memory
  Initial references to far memory have high latency, subsequent references are at near memory speeds
  Standard technology, caches can be large and cheap
Advantages
  System can work well with less/no optimization of O/S and applications
  Useful for some styles of shared memory use
Disadvantages
  Extra hardware complexity and cost
Notes: 24

## Slide 25
I/O Considerations
I/O via per-node PCI bus
  More non-uniformities to cope with
“Far” DMA undesirable
  Costly or disallowed on some architectures
“Fully connected I/O” desirable
  Attachment to each node in system
  Improves performance and resilience
  Examples - SSA (Serial Storage Architecture) and FibreChannel
Notes: 25

## Slide 26
NUMALiiNE Memory Map
Size estimates assume 4GB memory per node.
640K
Extended
Memory
(above 4G)
Extended
Memory
(EISA)
Extended
Memory
(ISA)
Compatibility
Area
General NUMALiiNE
Memory Map
General PC
Memory Map
Unused
High Global Memory
Possible PCI space overlays
on 16K boundaries. (Hides the
memory behind it.)
Low Global Memory
PCI Memory
-likely 32
M per node
64G
1M
16M
4G
0
This slide courtesy of Data General
Notes: 26
26

## Slide 27
NUMALiiNE Memory Map Example
Mem
Mem
Near memory-space resource (mem, PCI, CSR, ect.)
Far non-cacheable PCI memory
Far cacheable memory
Unused memory space
CSR
In/Out
AT Hole:
FFFFF
thru
A0000
Remapped into:
7xxxx
0xxxx
1xxxx
2xxxx
3xxxx
4xxxx
5xxxx
6xxxx
512 KB
32 MB
space
divided
between
two
PBs
Above 4GB
:
Mapped in
512MB
increments
Below 4GB
:
Mapped in
32MB
increments
0
unused
64GB
Integer
512MB
size
4GB
Node 4
Node 3
Node 2
Node 1
Apic
PCI
Mem
Mem
Apic
PCI
Mem
Mem
Apic
PCI
Mem
MC
Mem
Mem
Apic
PCI
32M region private
to each node
This slide courtesy of Data General
Notes: 27
27

## Slide 28
Finding out more
  http://www.dg.com
  http://www.sequent.com
  http://www.sunrise.scu.edu/
  Research from Stanford, Rochester, Toronto etc.
Notes: 28

## Slide 29
NUMA Impact on O/S
The Operating System is key
  It needs to understand the non-uniformities and behave accordingly
  Data layout, access patterns crucial
  For SCO, various mechanisms, flexible policies
    Allow for a range of target machines
Notes: 29

## Slide 30
Operating System Styles
There are two starting points
  But a convergence of end points
Style 1 - Monolithic
  Start with standard SMP kernel
  Incrementally loosen
Style 2 - Distributed
  Start with distributed O/S
  Incrementally tighten
Notes: 30

## Slide 31
The Gemini approach to NUMA
A single kernel
  Performance, incrementalism
Initially targeted at Intel Pentium Pro
  Should work well on a variety of such machines
Collaboration with partners
Notes: 31

## Slide 32
The O/S and scheduling
Limit process migration
  Affinity as per current processor affinity
  Exploits local memory, far memory cache
Static load balancing
  At fork or exec time
Dynamic load balancing
  Needed for longer term usability
  Daemon process
Notes: 32

## Slide 33
Virtual Memory Techniques
“Near” allocation wherever possible
  Kernel data structures as well as user pages
Replication of read-only memory
  Kernel and program text, read-only data
  Must handle read-only becoming read-write
Balanced allocation where required
  For global structures, balance across nodes
  Best for some application shared memory
Notes: 33

## Slide 34
More VM changes
Use of large physical memory
  36 bit address mode of Pentium Pro
  Backwards compatibility glue where needed
Reduce use of kernel virtual space
  It’s becoming a scarce resource!
Notes: 34

## Slide 35
I/O framework
I/O paths understand placement of memory buffers and controllers
  Use of near controllers where possible
  Copy and/or reschedule where appropriate
    Configurable “deflection layer”
New DDI8 specification
  Compatibility layers for DDI7 drivers
Notes: 35

## Slide 36
Multi Path I/O
PDI infrastructure enhancement
  Layering, scalability etc
MPIO deflection layer
  For load balancing and HA failover
  Not just for NUMA systems
Administrative tools
Notes: 36

## Slide 37
More O/S changes
Networking, STREAMS etc.
  More NUMA performance changes
Large filesystems
  Not all filesystems, just a selected subset
Careful attention to data layout
  Privatize by restructuring for better locality
    break up global data structures
    Group data by reference patterns
  Localize data to reduce far accesses
  Reduce False Sharing of cache lines
Notes: 37

## Slide 38
RAS features
Most features are not NUMA specific
  Abbreviated crash dumping (would you like to wait for 8 GBytes to be saved?)
  Diagnostics
  Alternate configurations for quick reboot
  Exploit resilience features of new I/O interconnects such as FibreChannel
  Various hot plug abilities
  Plus more….
Notes: 38

## Slide 39
O/S Summary
Success of Gemini on NUMA platforms is dependent on the O/S running existing applications well.
This has required major O/S work
Many of these changes are also beneficial in the general case
Notes: 39

## Slide 40
Implications for Developers
Most people
  Don’t need to worry
Performance critical applications
  May give O/S guidance via APIs
Performance critical drivers
  Another rev of DDI/DDK
  Physical address size > virtual address size
  May need to grapple with 64 bit PCI
Notes: 40

## Slide 41
Who would use the APIs?
Performance critical applications with..
  Substantial use of shared memory
  Unusual resource access patterns
  Need to control process placement
Example:
  Shared memory is probably allocated wherever the first page fault occurs.
  Database indexes should be balanced across the memory to prevent hot-spots.
  So the database uses an API to specify this.
Notes: 41

## Slide 42
NUMA APIs
Guide O/S’s placement decisions
Likely to include…
  New fcntl() variants
  New shmget() flags
  Mechanisms for guiding fork() and exec()
Still under development
  SCO welcomes input
Notes: 42

## Slide 43
DDI 8
DDI 8 is still under development
  Various new features
  Older drivers still supported.
Main change for NUMA is >4GB addresses
SCO working with partners
  Defining the interface
  Ensuring availability of key drivers
Notes: 43
43