## Slide 1
IPv6: Migration to a new Internet Protocol
Harvey Thompson
Software Engineer
Notes: 1

## Slide 2
What is IPv6?
Why is IPv6 needed?
When will IPv6 become available?
How do we migrate to IPv6?
Overview
Notes: 2

## Slide 3
New version of the Internet Protocol (IP)
  Larger address space (128 bit)
  Improved address hierarchies and routing
  Simplified header processing
  Improved option support
Compatible with IPv4
What is IPv6?
Notes: 3

## Slide 4
The Internet is growing fast
  The IPv4 address space will run out soon
  The backbone routers may collapse sooner
Support for new and future technologies
Why is IPv6 needed?
Notes: 4

## Slide 5
From SCO, partially in Gemini (mid 1997)
  The user level socket APIs will support IPv6
  The O/S services will be “IPv6 ready”
Later on SCO will ship full functionality
  Protocol (device and kernel) support
  Additional IPv6 services and APIs
Industry support over next few years
When will IPv6 become available?
Notes: 5

## Slide 6
Migrate existing networked applications in mid 1997
  Add support for IPv6 address formats and options
  Test using IPv4 node address (::FFFF:d.d.d.d)
Most migrated applications should “just work” when full implementation arrives
Specialised applications may then need more changes and testing
How do we migrate to IPv6?
Notes: 6

## Slide 7
Extends existing BSD style socket APIs
New address data structures
Support in socket functions
New name/address functions
Other features
  Flowinfo
  Socket options
  Special addresses
The IPv6 socket API Draft Overview
Notes: 7

## Slide 8
New protocol and address family
  PF_INET6
  AF_INET6
New IPv6 address structure
  struct in6_addr
    128 bits of address
New address data structures (1)
Notes: 8

## Slide 9
New sockaddr structure
  struct sockaddr_in6
    16 bit family (or 8 bit length, 8 bit family)
    16 bit port
    32 bit flowinfo
    128 bit address
New address data structures (2)
Notes: 9

## Slide 10
To create PF_INET6
  socket()
Functions taking sockaddr_in6
  bind(), connect()
  sendmsg(), sendto()
Functions returning sockaddr_in6
  accept(), recvfrom(), recvmsg()
  getpeername(), getsockname()
Support in socket functions
Notes: 10

## Slide 11
Usually written as eight 16 bit hex numbers, separated by a colon
  1080:0000:0000:0000:0008:0800:0200c:417a
Leading zeroes in each field not needed
  1080:0:0:0:8:800:200c:417a
One group of multiple 16 bit zeroes may be written as two colons
  1080::8:800:200c:417a
New name/address functions (1) IPv6 Address Notation
Notes: 11

## Slide 12
Special case for IPv4 embedded addresses, last two fields can be written in IPv4 notation
  ::150.126.252.1
  ::FFFF:150.126.252.1
IPv6 tunneled over IPv4 uses former
(or IPv4-compatible IPv6 address)
IPv6 talking to IPv4 uses latter
(or IPv4-mapped IPv6 address)
New name/address functions (2) IPv6 Address Notation (continued)
Notes: 12

## Slide 13
Convert hostname to address(es)
  getaddrinfo() (POSIX 1003.1g)
Convert address to hostname
  getnameinfo()
Check for embedded IPv4 address
  inet6_isipv4addr()
New name/address functions (3)
Notes: 13

## Slide 14
Convert address string to address structure
  inet_pton()
Convert address structure to address string
  inet_ntop()
  INET_ADDRSTRLEN
  INET6_ADDRSTRLEN
New name/address functions (4)
Notes: 14

## Slide 15
Flowinfo
  IPV6_FLOWINFO_FLOWLABEL (24 bit mask)
  IPV6_FLOWINFO_PRIORITY (4 bit mask)
    IPV6_PRIORITY_* (8 congestion, 8 real time)
Socket options (IPPROTO_IPV6)
  IPV6_ADDRFORM
  IPV6_UNICAST_HOPS (outgoing)
  IPV6_MULTICAST_IF (outgoing)
  IPV6_MULTICAST_HOPS (outgoing)
  IPV6_MULTICAST_LOOP (outgoing)
Other features (1)
Notes: 15

## Slide 16
  IPV6_ADD_MEMBERSHIP (incoming)
  IPV6_DROP_MEMBERSHIP (incoming)
  struct ipv6_mreq
    128 bit multicast group address
    128 bit interface address
Special Address
  in6addr_any, IN6ADDR_ANY_INIT
  in6addr_loopback, IN6ADDR_LOOPBACK_INIT
Other features (2)
Notes: 16

## Slide 17
The API definitions are work in progress
  The draft will eventually become an RFC
The standards have room for expansion
  Keep an eye on new RFCs that update or outdate existing RFCs
This means things will probably change
  Further Reading is probably out of date
  This presentation is probably out of date
  SCO’s plans for IPv6 may well change
This is out of date!
Notes: 17

## Slide 18
“IPng Home Page”
http://playground.sun.com/pub/ipng/html/ipng-main.html
“Basic Socket Interface Extensions for IPv6”
ftp://ds.internic.net/internet-drafts/draft-ietf-ipngwg-bsd-api-05.txt
“Internet Protocol, Version 6 (IPv6) Specification”
ftp://ds.internic.net/rfc/rfc1883.txt
“IP Version 6 Addressing Architecture”
ftp://ds.internic.net/rfc/rfc1884.txt
“Internet Control Message Protocol (ICMPv6) for the Internet Protocol Version 6 (IPv6)”
ftp://ds.internic.net/rfc/rfc1885.txt
Plus many more…
ftp://ds.internic.net/rfc/rfc-index.txt
ftp://ds.internic.net/internet-drafts/1id-index.txt
Further Reading
Notes: 18